Rev 2.00 Edger white board wiring rev 0.50 10/28/2022

Espressif dev board PHYSICAL PINS:

Length	(cm)	Color	From	To
2.5	Blk	30 “G”	breadboard ground rail (blue line)
2.5	Red	18 “3.3V”	breadboard power rail (red line)
7.9	Org	14 “0”	FPGA physical pin 8 “SCL”
8.0	Ylw	13 “1”	FPGA physcial pin 9 “SDA”
7.6	Wht	4 “18”	JTAG	USB D- (Adafruit breakout)
8.2	Gry	5 “19”	JTAG USB D+ (Adafruit)

Adafruit USB breakout:

5.0	Blk	ground rail	JTAG USB Gnd

Renesas FORGEFPGA SLG47004V-DIP PHYSICAL PINS:

2.5	Red	power rail	FPGA pin 1 “VDD”
2.5	Blk	ground rail	FPGA pin 11 “GND”

Other:

6.8	Red	power rail 1	power rail 2 (red lines)